## Slide 1
Measured Internal Temperatures in UK:
A descriptive Time Series Analysis & Modelling approach
Methodology: 4 Funerals and a Wedding
Argyris Oraiopoulos 3rd Year PhD
LoLo Student-Led Conference
16 June 2016
Supervisors: Dr Tom Kane, Dr Steven Firth, Prof Kevin Lomas

## Slide 2
Dataset
Research Question
Year 1 – Methods 1 & 2
Year 2 – Methods 3 & 4
Year 3 – Method 5
Conclusions
Future work
Overview

## Slide 3
Hourly recorded internal air temperatures
Living rooms and main Bedrooms
228 homes in Leicester, UK
201 Bedrooms, 210 Living rooms
411 Free-floating spaces (No heating, No mechanical cooling)
62 Days, from 1st July till 31st August 2009
Number of occupants
Age of Oldest occupant
Type of Tenure
House Type
House Age
Wall Type
Loft Insulation
*All images licenced under Creative Commons
Dataset

## Slide 4
t
Can we use empirical data
to predict internal temperatures in buildings
during summer conditions?
Objectives
Analyse data
Understand internal room temperature formation
Construct statistical models
Forecast future temperatures
Research Question
*All images licenced under Creative Commons

## Slide 5
High correlation between daily mean internal and Trm across sample (R2 = 0.87)
Intercept and Slope from best fit of daily mean internal against Trm for every house
Relationship between intercept/slope of best fit and house characteristics.
1
0
2
Daily mean of Internal temperature (°C)
Running mean external temperature, Trm (°C)
  Trmt = (1-α) (Tt + α Tt-1 + α2 Tt-2 + α3 Tt-3.....)
Method 1: Statistical Modelling – Internal temperature Vs External
Year 1 – Method 1
Chart: House Type
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159 | 160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175 | 176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191 | 192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230
Detached | 7.9572 | 4.1721 | 3.7081 | 7.6175 | 11.6989 | 4.437 | 7.7453 | 4.3245 | 8.254 | 4.3764 | 5.5068 | 12.1317 | 12.6991 | 10.0537 | 7.9311 | 11.8477 | 8.6966 | 9.9154
End Terraces | 9.3079 | 6.7279 | 2.4441 | 10.9243 | 7.1675 | 7.2647 | 11.6899 | 11.4971 | 9.5993 | 7.2835 | 6.3658 | 12.896 | 7.8353 | 8.4087 | 6.1432 | 14.035 | 12.1847 | 10.3966 | 14.2201 | 6.9337 | 10.1115 | 12.623
Mid Terraces | 15.2731 | 8.4319 | 7.4729 | 8.4823 | 10.196 | 5.2813 | 13.0565 | 6.3251 | 17.9145 | 7.8854 | 7.0613 | 10.2583 | 12.2759 | 10.8335 | 9.1678 | 8.8855 | 8.0802 | 9.4193 | 6.9148 | 11.1945 | 12.4556 | 7.3372 | 12.3989 | 11.4796 | 10.4232 | 10.8018 | 9.8305 | 9.7895 | 12.7468 | 10.4949 | 9.8587 | 10.7991 | 9.9414 | 10.0127 | 8.5482 | 10.3548 | 9.9782 | 10.3559 | 6.0466 | 12.9697 | 8.9935 | 10.8419 | 10.6392 | 7.0267 | 10.3081 | 11.967 | 13.0905 | 10.8435 | 12.537 | 7.183 | 15.0072 | 15.5319 | 7.2497
Flats | 12.3163 | 14.8593 | 11.3586 | 10.6107 | 5.4351 | 12.6916 | 8.8572 | 13.1866 | 6.1293 | 12.762 | 6.5619 | 13.2576 | 9.583 | 10.9091 | 9.286 | 11.3657 | 15.3051 | 4.3023 | 10.3133 | 13.9065 | 13.9804 | 10.4421 | 11.7695 | 14.9034 | 9.5811 | 14.9056 | 7.7707
Chart: House Type
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159 | 160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175 | 176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191 | 192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230
Detached | 0.79404 | 1.0972 | 1.0207 | 0.7931 | 0.69434 | 1.0236 | 0.86139 | 0.99809 | 0.69554 | 0.92148 | 1.0182 | 0.65318 | 0.54515 | 0.74834 | 0.81631 | 0.67829 | 0.81007 | 0.72749
End Terraces | 0.73328 | 0.81229 | 1.0247 | 0.75864 | 0.87535 | 0.90088 | 0.70243 | 0.62037 | 0.80617 | 0.86508 | 0.93715 | 0.58688 | 0.78717 | 0.82888 | 0.89256 | 0.6119 | 0.64828 | 0.7611 | 0.57335 | 0.83434 | 0.70436 | 0.64361
Mid Terraces | 0.48935 | 0.84496 | 0.83922 | 0.6892 | 0.72069 | 0.90521 | 0.54118 | 0.83675 | 0.40109 | 0.81663 | 0.88815 | 0.72864 | 0.65718 | 0.65942 | 0.76195 | 0.7347 | 0.6918 | 0.7112 | 0.9124 | 0.69391 | 0.64095 | 0.89526 | 0.69232 | 0.65825 | 0.79758 | 0.72272 | 0.71774 | 0.66154 | 0.63025 | 0.7843 | 0.86191 | 0.76163 | 0.85292 | 0.81861 | 0.74643 | 0.71656 | 0.69017 | 0.67267 | 0.94333 | 0.62115 | 0.82205 | 0.67223 | 0.70972 | 0.99176 | 0.73305 | 0.58967 | 0.60642 | 0.74146 | 0.61809 | 0.8402 | 0.50849 | 0.47291 | 0.83814
Flats | 0.69242 | 0.53752 | 0.67105 | 0.81117 | 0.8252 | 0.64186 | 0.74543 | 0.6297 | 0.98198 | 0.55055 | 0.97591 | 0.69462 | 0.70784 | 0.71201 | 0.86388 | 0.5855 | 0.5821 | 1.0242 | 0.66619 | 0.55743 | 0.58755 | 0.81505 | 0.77536 | 0.56959 | 0.82528 | 0.55208 | 0.90551
Conclusions
No correlations found between intercept/slope and house type/house age/wall type
Correlation NOT uniform across sample
Nothing significant - Nothing Strong
Y = Intercept + Slope * X
Tools: Excel, SPSS

## Slide 6
Chart: 20 Semis - Living rooms
 | 7.3109 | 6.9044 | 8.4354 | 6.4003 | 6.2395 | 9.1215 | 5.8995 | 9.9557 | 13.698 | 10.894 | 8.4917 | 11.7675 | 14.2432 | 10.3325 | 14.9416 | 13.4414 | 14.9697 | 12.297 | 12.3163 | 14.3022
Chart: Heat Gains to Losses ratio (ascending order)
 | 0.82794 | 0.84224 | 0.76575 | 0.93599 | 0.92344 | 0.78556 | 0.90094 | 0.72945 | 0.5042 | 0.72839 | 0.78559 | 0.59284 | 0.5012 | 0.75548 | 0.48697 | 0.60497 | 0.46328 | 0.68854 | 0.69242 | 0.57845
SAP 2009 Heat gains to losses ratio
Relationship between Heat gains to losses ratio and intercept/slope of best fit line between daily mean internal and Trm
Year 1 – Method 2
Method 2: Statistical Modelling - Heat gains to losses ratio based on SAP 2009 calculation
Conclusions
Identification of weak trend
Sample decrease (230 homes to 190)
Using SAP – Extended number of inputs (Volume, U-values, orientation, glazing, etc.)
Assumptions – Uncertainty
Tools: Sap 2009, Excel
*Permission to use SAP 2009 given by Dr David Allinson

## Slide 7
Year 2 – Method 3
Method 3: Times Series Analysis & Modelling – Univariate ARIMA
Tools: SPSS, Excel
Chart: Date
Modelled | 19.353 | 19.171 | 19.015 | 18.878 | 18.741 | 18.649 | 18.57 | 18.493 | 18.552 | 18.685 | 18.751 | 18.845 | 18.964 | 19.177 | 19.425 | 19.605 | 19.832 | 20.218 | 20.143 | 19.739 | 19.674 | 19.692 | 19.791 | 19.356 | 19.126 | 18.946 | 18.792 | 18.657 | 18.52 | 18.43 | 18.351 | 18.275 | 18.334 | 18.468 | 18.533 | 18.628 | 18.747 | 18.96 | 19.208 | 19.388 | 19.616 | 20.001 | 19.927 | 19.523 | 19.457 | 19.476 | 19.574 | 19.14
Chart: Hours
Modelled | 19.493 | 19.353 | 19.171 | 19.015 | 18.878 | 18.741 | 18.649 | 18.57 | 18.493 | 18.552 | 18.685 | 18.751 | 18.845 | 18.964 | 19.177 | 19.425 | 19.605 | 19.832 | 20.218 | 20.143 | 19.739 | 19.674 | 19.692 | 19.791 | 19.356 | 19.126 | 18.946 | 18.792 | 18.657 | 18.52 | 18.43 | 18.351 | 18.275 | 18.334 | 18.468 | 18.533 | 18.628 | 18.747 | 18.96 | 19.208 | 19.388 | 19.616 | 20.001 | 19.927 | 19.523 | 19.457 | 19.476 | 19.574 | 19.14
Xt = φt Xt-1 + …. + φp Xt-p + εt – ϑq εt-1 – ….. – ϑq εt-q
Auto Regressive
(Past behaviour)
Error
Moving Average
(Random shocks)
For Yt , Xt = Yt - Yt-1

## Slide 8
Year 2 – Method 4
Method 4: Times Series Analysis & Modelling – Multivariate ARIMA
Tools: EViews, SPSS, Excel
Direction of forecasts
Chart: Date
Chart: Date

## Slide 9
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – 1 living room

## Slide 10
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – 2 living rooms

## Slide 11
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – 4 living rooms

## Slide 12
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – 30 living rooms

## Slide 13
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – 132 Living rooms

## Slide 14
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling –

## Slide 15
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Descriptive Decomposition
measured
trend
residual
cyclical variation
Additive Model
Yt = Tt + Ct + Rt
Initial Data Analysis
Adjustments
Identification
Estimation
Model Checking
Forecasting
Yt
Tt
Ct
Rt
Tools: SPSS, VBA, Excel, (Box & Jenkins, 1976)
Chart: Internal Air Temp. (°C)
Chart: Date
Chart: Internal Air Temp. (°C)

## Slide 16
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 17
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 18
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 19
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 20
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 21
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Modelling of Trend
Tools: SPSS, VBA, Excel
Chart: Date
,

## Slide 22
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Modelling of Trend
Tools: SPSS, VBA, Excel
Chart: Date
Simple Linear Regression for Modelled Trend :

## Slide 23
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Cyclical (diurnal) component
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 24
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Cyclical (diurnal) component
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 25
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Cyclical (diurnal) component
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 26
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Modelling of Cyclical (diurnal) component
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 27
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Final Model (Measured vs. Modelled)
Tools: SPSS, VBA, Excel
Chart: Date
Chart: Internal Air Temp. (ºC)
Chart: Internal Air Temp. (°C)
Chart: Internal Air Temp. (°C)
Chart: Internal Air Temp. (ºC)
Chart: Date

## Slide 28
Conclusions – Future Work
Chart: Internal Air Temp. (°C)
Modelled | 19.353 | 19.171 | 19.015 | 18.878 | 18.741 | 18.649 | 18.57 | 18.493 | 18.552 | 18.685 | 18.751 | 18.845 | 18.964 | 19.177 | 19.425 | 19.605 | 19.832 | 20.218 | 20.143 | 19.739 | 19.674 | 19.692 | 19.791 | 19.356 | 19.126 | 18.946 | 18.792 | 18.657 | 18.52 | 18.43 | 18.351 | 18.275 | 18.334 | 18.468 | 18.533 | 18.628 | 18.747 | 18.96 | 19.208 | 19.388 | 19.616 | 20.001 | 19.927 | 19.523 | 19.457 | 19.476 | 19.574 | 19.14
Chart: Internal Air Temp. (ºC)
Chart: Date
Conclusions
Don’t give up ! (despite suggestions)
R2 Improvement (0.15 – 0.82)
BUT what does R2 mean?
(overheating)
Solution can be too simple to look at
Univariate ARIMA
Multivariate ARIMA
Descriptive Decomposition

## Slide 29
Future Work
Future Work
Test more Cyclical Models (include solar, sinusoidal, percentiles)
Future Weather Scenario (2030, 2050, 2080)
Dynamic Thermal Simulation Validation
Application of Model on different dataset (Passive House, etc.)

## Slide 30
Questions / Discussion
Thank you
a.oraiopoulos@lboro.ac.uk
www.lolo.ac.uk
Argyris Oraiopoulos
@AOraiopoulos

## Slide 31
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Final Model
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 32
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Final Model incl. Solar Component (Tsol-air)
Tools: SPSS, VBA, Excel
Chart: Date

## Slide 33
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling - Identification of Trend
Chart: Date
Exponentially weighted moving average of the external daily mean air temperature ( ), using the past 15 days () for all values of alpha ()

## Slide 34
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling - Identification of Trend
Chart: Date
Exponentially weighted moving average of the external daily mean air temperature ( ), using for all values of between 1 and 15.

## Slide 35
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Trend Modelling
Chart: Past days (m)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
α=0.1 | 0.5825 | 0.58974 | 0.59037 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043 | 0.59043
α=0.2 | 0.62699 | 0.65174 | 0.65608 | 0.65684 | 0.65705 | 0.65708 | 0.65709 | 0.65709 | 0.65709 | 0.65709 | 0.65709 | 0.65709 | 0.65709 | 0.65709 | 0.65709
α=0.3 | 0.66263 | 0.70921 | 0.72129 | 0.7245 | 0.7258 | 0.72617 | 0.72623 | 0.72624 | 0.72624 | 0.72625 | 0.72625 | 0.72625 | 0.72625 | 0.72625 | 0.72625
α=0.4 | 0.69106 | 0.75921 | 0.78178 | 0.78966 | 0.79401 | 0.7957 | 0.79611 | 0.7962 | 0.79625 | 0.79627 | 0.79627 | 0.79627 | 0.79627 | 0.79627 | 0.79627
α=0.5 | 0.71375 | 0.80029 | 0.8335 | 0.84745 | 0.85707 | 0.86181 | 0.86329 | 0.86372 | 0.86401 | 0.86414 | 0.86418 | 0.8642 | 0.86421 | 0.86422 | 0.86422
α=0.6 | 0.73188 | 0.83233 | 0.87369 | 0.89298 | 0.90836 | 0.91711 | 0.92019 | 0.92132 | 0.9223 | 0.92289 | 0.92315 | 0.92333 | 0.92348 | 0.92356 | 0.9236
α=0.7 | 0.74641 | 0.85608 | 0.90141 | 0.92294 | 0.94074 | 0.95035 | 0.95246 | 0.95303 | 0.9545 | 0.95571 | 0.95647 | 0.95727 | 0.95807 | 0.95864 | 0.95897
α=0.8 | 0.7581 | 0.87276 | 0.91741 | 0.93656 | 0.94944 | 0.95008 | 0.94103 | 0.93362 | 0.93021 | 0.928 | 0.92671 | 0.92719 | 0.9285 | 0.92984 | 0.93088
α=0.9 | 0.76753 | 0.8837 | 0.92353 | 0.93563 | 0.93461 | 0.912 | 0.87426 | 0.84328 | 0.81972 | 0.79825 | 0.77988 | 0.76713 | 0.7568 | 0.74781 | 0.73992
Chart: Past days (m)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
α=0.9 | 0.76753 | 0.8837 | 0.92353 | 0.93777 | 0.9497 | 0.95492 | 0.95446 | 0.95412 | 0.95536 | 0.95652 | 0.9573 | 0.95824 | 0.95923 | 0.95999 | 0.96047
R2 values between of a living room (116131) and for varying m values between 1-15 days and varying values between 0.1-0.9

## Slide 36
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Trend R2 values Histograms

## Slide 37
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Trend α values Histograms

## Slide 38
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Trend m values Histograms

## Slide 39
Year 3 – Method 5
Method 5: Times Series Analysis & Modelling – Identification of Trend
Tools: SPSS, VBA, Excel
Chart: Date